## Slide 1: A faster, leaner Assa Abloy warehouse in the same building
PROJECT OTM · PREPARED FOR DHL SUPPLY CHAIN, BEMMEL
Our redesign of receiving, storage, picking and shipping — and what it means for service, cost and growth
Group 3 · Vidhi (Receiving) · Gleb (Storage) · Arnau (Picking) · Rachel Selvarathnam (Shipping)
HAN University of Applied Sciences, OPERMB04 · based on Assa Abloy warehouse data, April–June 2025
Notes: PRESENTER: Gleb (Storage) · about 0:15 Good morning. We are Group 3. Over the last weeks we redesigned the Assa Abloy warehouse that DHL runs in Bemmel. Each of us owns one process — Vidhi receiving, me storage, Arnau picking and Rachel shipping — and each of us presents their own part.

## Slide 2: Our design lets DHL keep its promise to Assa Abloy at a lower cost: 65% of orders out within 24 hours, 62% fewer picker-hours, in the same building
EXECUTIVE SUMMARY
Source: WMS data April–June 2025 (Assa Abloy & DHL Supply Chain, 2025); design values modelled in Deliverables 2 and 3; all calculations step by step in the appendix
Gleb · presenter
Today
DHL ships ~640 order lines a day for Assa Abloy from 4,354 different items. All orders are released at once in the evening: picking peaks at 08:00, only 49.9% of lines are staged on time and 37% of orders leave within 24 hours.
Our answer
A one-way flow from dock to trailer: a fast-pick area for the 1,409 best-sellers, batch picking with a put-to-light wall, and three waves planned back from fixed trailer departures. It fits in 6,731 of the 7,000 m².
What DHL gets
65% of orders out within 24 h and a ≥ 98% on-time target; ~12 instead of ~31 picker-hours a day (€101k a year); €3.09 per order line; trucks and pickers fully separated.
How to start
With the low-cost process changes (€0.16M, payback ~1.6 years). The racking decision comes last. Main risk: stock growth fills the racks in ~4 months.
WHAT DHL GETS
65%
of orders out within 24 h — modelled (today 37%, measured)
≥ 98%
of lines on time — target of the wave plan (today 50%)
−62%
picker-hours a day: ~31 → ~12 (modelled)
1.6 yrs
payback: €157k invested ÷ €101k saved a year
Notes: PRESENTER: Gleb (Storage) · about 0:50 Our answer first. Today about 640 order lines a day go out, but all orders are released at once in the evening, so the floor is overloaded at eight in the morning and only half of the lines are staged on time. We redesigned the warehouse around the flow: a fast-pick area for the best-sellers, batch picking, a put-to-light wall and three waves planned backwards from fixed trailer departures. For DHL that means 65% of orders out within 24 hours instead of 37%, about 12 instead of 31 picker-hours a day, and it all fits in the current building. Arnau first shows where these numbers come from. IF ASKED HOW WE CALCULATED IT: Every number on this slide is calculated step by step on the appendix slides 'How we calculated' — storage, picking, service, money, running cost and receiving.

## Slide 3: Every number comes from Assa Abloy's own warehouse data, run through simple models — every assumption is written down with its source
HOW WE GOT OUR NUMBERS
Source: WMS data April–June 2025 (Assa Abloy & DHL Supply Chain, 2025); assumption register (data/assumptions.json) and source register; Deliverable 3 calculation workbook
Arnau · presenter
1 Data
2 Assumptions
3 Models
4 Checks
MEASURED
39,069
order lines in the WMS, April–June 2025
8,781 orders over 61 working days
3 stock snapshots: up to 11,015 loads in 8,512 places
~15 outbound trailers a day, with arrive and dispatch times
WRITTEN DOWN
46
assumptions, each with its reason and source
25 s per picked line, walking 0.8 m/s, +10% for delays
€20 per hour for an operator (course teacher)
racking €130 per place (benchmark €80–200)
CALCULATED
8,774
real orders re-timed with the new wave plan
pick time per tour: set-up + walking + time per line
storage growth from the three snapshots
every cost formula live in the D3 workbook
TESTED
+€86k
a year if labour costs €28 instead of €20 per hour — our biggest uncertainty
today and design compared on the same orders
racking price and productivity ±20% also tested
stress test at 150–250% volume
How to read our numbers: measured = straight from Assa Abloy's data · modelled = our calculation on the same data · target = what the design is built to reach
Notes: PRESENTER: Arnau (Picking) · about 0:45 Before the results, where do our numbers come from? First, data: the warehouse system's own records for April to June 2025 — 39,069 order lines, three stock snapshots and the trailer times. Second, assumptions: where the data has no answer, for example how many seconds a pick takes or what an hour of labour costs, we wrote the assumption down with its source — 46 of them. Third, models: simple calculations on the same data. For example, we re-timed all 8,774 real orders with our new wave plan. Fourth, checks: we compare today and the design on the same orders, and we tested the biggest uncertainties. On every slide we show the calculation at the bottom, and the appendix has every step. IF ASKED HOW WE CALCULATED IT: Assumptions: 46 in data/assumptions.json, each with a reason, a source and an impact rating. Sensitivity: labour rate €20–28/h changes the yearly cost by €86k.

## Slide 4: Today all orders are released at once: picking peaks at 08:00, half the lines ship late and the racks are almost full
TODAY · OUR SOLUTION · PROCESSES · VALUE FOR DHL · ROADMAP
Source: WMS data April–June 2025 (Assa Abloy & DHL Supply Chain, 2025); picker-hours modelled (Deliverable 3 §2.2); step by step: appendix "How we calculated: picking"
Arnau · presenter
When orders arrive vs when lines are picked
share of the day's total per hour of the day, % — measured, April–June 2025
Chart: hour of the day
| 06 | 07 | 08 | 09 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18
Orders arriving | 0.5 | 0.7 | 6.7 | 7.6 | 8.8 | 7.6 | 5.3 | 1.9 | 5.3 | 19.8 | 35.3 | 0.2 | 0
Lines picked | 7.1 | 11 | 14 | 12.4 | 10.6 | 8.7 | 12.3 | 10.7 | 9.2 | 3.8 | 0.2 | 0 | 0
Picking peaks at 08:00: 1.31× the average hour
55% of orders arrive 15:00–17:00, released together in the evening
What it costs DHL today
Service
49.9% of lines staged on time; 37% of orders out within 24 h, the slowest 10% take over 102 h
Cost
~31 picker-hours a day: every tour picks one order, and staff is planned for the 08:00 peak
Space
racks full in ~4 months at the current growth; slotting matches demand for only 49% of items
The cause: how work is released and picked — not a lack of space.
HOW WE CALCULATED IT Measured: on time = order lines the WMS did not flag 'LATE'; within 24 h = trailer left − order received, per order (8,774 orders); arrivals and picks counted per hour. Modelled: picker-hours = time per tour × tours, one order per tour today (23.77 h), × 1.31 because staff is planned for the 08:00 peak = 31.1 h.
Notes: PRESENTER: Arnau (Picking) · about 1:30 This chart is the core of the problem. The grey bars show when orders arrive: 55% come in between three and five in the afternoon. They are all released in one go in the evening, so the red line — picking — peaks at eight the next morning. For DHL this costs on three fronts. Service: only 49.9% of lines are staged on time and 37% of orders leave within 24 hours — both measured in the data. Cost: about 31 picker-hours a day, which we modelled. Space: the racks are almost full. The cause is the way work is released and picked, so that is what our design changes. Vidhi shows the solution. IF ASKED HOW WE CALCULATED IT: On time: 49.9% of the 39,069 order lines are not flagged 'LATE' in the WMS (the definition is assumption A005, to confirm with DHL). Within 24 h: for each order, trailer dispatch time minus order arrival time. Picker-hours: we timed every order as its own tour, with picks spread over all aisles — 23.77 hours — and multiplied by 1.31, the 08:00 hour divided by the average picking hour, because staff is planned for the peak.

## Slide 5: One-way flow from dock to trailer in 6,731 m² — the design fits the current 7,000 m² building
TODAY · OUR SOLUTION · PROCESSES · VALUE FOR DHL · ROADMAP
Source: team layout drawing, to scale (Deliverable 2 §2); option choice: team decision matrix (Deliverable 1 §15)
Vidhi · presenter
The route of an order line
1
Trailers unloaded and checked at R2 / R3
C
Containers unpacked at R1, built onto pallets
2
Reach truck puts the pallets away
3
Refills drop cases into the fast-pick area
4
Orders picked in waves, taken to packing
5
Sorted at the put-to-light wall and packed
6
Staged in the lane of its door and loaded
96%
of the 7,000 m² used
8,960
pallet places
3 + 5
doors in / out
3.75
of 5: best of three options
HOW WE CALCULATED IT 6,731 m² = all zones measured on the to-scale drawing, added up: racks 3,505 + odd/long goods 728 + fast-pick 500 + packing 450 + aisles 450 + 5 smaller zones 1,098. 8,960 places counted: 7,776 standard + 864 odd-size + 320 long. Option score = sum of weight × score (1–5).
Notes: PRESENTER: Vidhi (Receiving) · about 1:30 This is our layout, drawn to scale, with the route of one order line. Goods come in on the west wall: pallet trailers at doors R2 and R3, and loose containers at R1. The reach truck puts the pallets away in single-deep racks and refills the fast-pick row along the south wall from behind. Pickers work that row and bring the goods to packing, and orders wait in the lane of their shipping door on the east wall. Everything moves one way. It uses 96% of the 7,000 square metres, so no extra building is needed. We chose this from three options; full automation scored almost as high (3.70) but costs more and copes less well with two-metre items. IF ASKED HOW WE CALCULATED IT: Area: we measured every zone on the to-scale drawing and added them up — 6,731 m², 96% of 7,000. Places: counted on the drawing, 7,776 standard, 864 odd-size and 320 long-goods places. Option score: each option scored 1 to 5 on seven criteria, multiplied by the weight of the criterion and added up — B 3.75, C 3.70, A 3.05 (appendix 'Option choice').

## Slide 6: Receiving keeps pallet trailers and loose containers apart, so a 40 ft container is unloaded and palletised in ~3.3 hours
TODAY · OUR SOLUTION · PROCESSES · VALUE FOR DHL · ROADMAP
Source: inbound receipts April–June 2025 (Assa Abloy & DHL Supply Chain, 2025); dock-to-stock benchmark (Extensiv, n.d.); step by step: appendix "How we calculated: receiving"
Vidhi · Receiving owner
How it works
1
Pallet trailers at R2 / R3. Unloaded into a lane (A–B), counted, checked and scanned at the bench (C), then collected by the reach truck at the pick-up point (D).
2
Loose containers at R1. Cartons roll out on a conveyor (F); two people build 12 pallets at once, one per item (G), with room for 35 finished pallets (H) and a wrap-and-label station (I).
3
Flexible space. On big-container days half of the R2 area (E) joins the container zone: +131 m².
99
inbound loads a day — measured (busiest day 167)
41%
of loads come from Asia, loose in containers
97%
of containers fit the zone (91% without R2's half)
~1.5 h
dock-to-stock per pallet trailer — modelled (benchmark < 3.5 h)
HOW WE CALCULATED IT 99 loads a day = loads booked in during the 14 days before each stock snapshot ÷ receiving days (average of 3). Container 3.3 h = 20 min docking + 3 h unpacking by 2 people (assumption). Dock-to-stock 1.5 h = 20 min + 58 pallets × 1.2 min (2 reach trucks). Zone fit = m² needed by each of 568 containers vs 190 m².
Notes: PRESENTER: Vidhi (Receiving) · about 1:30 Receiving handles about 99 loads a day, and 41% come loose in containers from Asia. The key idea is to keep the two apart. Pallet trailers dock at R2 and R3: pallets go into a lane, are checked and scanned at the bench, and the reach truck collects them — letters A to D. Containers dock at R1: cartons roll out on a conveyor and two people build 12 pallets at once, one per item — F to I. On the few big-container days we lend half of the R2 area, so 97% of containers fit. A pallet trailer is in stock in about 1.5 hours, well inside the 3.5-hour benchmark. Gleb takes over from the pick-up point. IF ASKED HOW WE CALCULATED IT: Loads a day: in each of the three stock snapshots we counted the loads booked in during the 14 days before it and divided by the receiving days — 70.9, 108.2, 117.6 — and took the average, 98.9. It is a lower bound, because loads already shipped out are not visible. Container time: 20 minutes docking and paperwork plus 3 hours unpacking by two people, an assumption (A019). Dock-to-stock: 20 minutes plus 58.3 pallets times 1.19 minutes, because two reach trucks put away in parallel at 2.38 minutes each. Zone fit: for each of the 568 containers in the data, conveyor lane 24 m² plus 3 m² per item plus 1.9 m² per pallet plus 16 m² wrap-and-label, plus 30% walkways, compared with 190 m².

## Slide 7: 8,960 rack places hold today's peak at 84% full — but at the current stock growth they are full in about 4 months
TODAY · OUR SOLUTION · PROCESSES · VALUE FOR DHL · ROADMAP
Source: stock snapshots 1 April, 1 May and 1 June 2025 (Assa Abloy & DHL Supply Chain, 2025); step by step: appendix "How we calculated: storage"
Gleb · Storage owner
Pallet places at the peak (June 2025)
Chart: 
| Occupied today (measured) | Needed in our design | Rack places in our design
Pallet places | 8512 | 7507 | 8960
−1,005 places: 2,657 small, slow items move to bin shelving next to packing.
Risk: at +16% a quarter the racks are full in ~4 months (~6 with the 12th module). 21% of loads are over a year old: clear dead stock first.
How storage works
1
Every pallet reachable. Single-deep racks back-to-back, 8 levels, 10 aisles; one reach-truck type (ETV 216i).
2
A place by demand. Fast movers' reserve close to the fast-pick area, slow movers further away; heavy pallets low.
3
Safe refills from behind. 31 carton-flow bays: the reach truck refills from the back, pickers take from the front.
HOW WE CALCULATED IT Needed = 8,512 occupied (1 June) − 1,005 places freed by small parts = 7,507; 7,507 ÷ 8,960 = 84%. Growth = (8,512 ÷ 7,715)^1.5 − 1 = 15.9% per quarter (2 months scaled to 3). Months until full = ln(8,960 ÷ 7,507) ÷ ln(1.159) × 3 = 3.6.
Notes: PRESENTER: Gleb (Storage) · about 1:30 Storage keeps every pallet and keeps the pick faces full. At the June peak 8,512 pallet places were in use. We move 2,657 small, slow items to bin shelving, which frees 1,005 places, so the design needs 7,507 of its 8,960 places — 84% full. All racks are single-deep, so every pallet can be reached without moving another. The fast-pick area is refilled from behind, so reach trucks and pickers never share an aisle — good for safety. The risk for DHL: stock grew about 16% in one quarter, so at that rate the racks are full in about 4 months. Clearing dead stock with Assa Abloy is the first lever; a 12th rack module is kept in reserve. IF ASKED HOW WE CALCULATED IT: Occupied places come straight from the three stock snapshots: 7,715, 8,149, 8,512. Freed places: rack places that hold only small, slow items — whole stock up to 50 litres, each item up to 20 litres, 15 kg and 60 cm, class C. Growth: 8,512 divided by 7,715 is the growth over two months; to the power 1.5 turns it into a quarter: 15.9%. Months until full: how many quarters of that growth fit between 7,507 and 8,960 — the natural log of the ratio divided by the natural log of 1.159, times 3 months: 3.6.

## Slide 8: Batch picking from a fast-pick area cuts picking from ~31 to ~12 picker-hours a day
TODAY · OUR SOLUTION · PROCESSES · VALUE FOR DHL · ROADMAP
Source: model on WMS order lines April–June 2025 (Assa Abloy & DHL Supply Chain, 2025) (Deliverable 3 §2.2); batching (de Koster et al., 2007); step by step: appendix "How we calculated: picking"
Arnau · Picking owner
Picker-hours on an average day
modelled on the same order lines
Chart: 
| Today: 31.1 h | Our design: 11.7 h
Picking work | 23.773 | 11.7
Extra staff for the 08:00 peak | 7.37 | 0
How it works
1
Split orders by size. 84% of orders are small and go on a trolley with 6 totes; the other 16% carry 88% of the volume and are picked straight onto a pallet.
2
Best-sellers close by. The 1,409 best-sellers sit in the fast-pick area: 71% of lines are picked there, with ~14 m of walking per line.
3
Batch, then sort. One trolley tour picks ~31 lines for many orders; the put-to-light wall (120 slots) sorts them into orders and checks every item.
4
Three waves a day. Instead of one evening release — no 08:00 rush; the first wave starts at 06:00.
HOW WE CALCULATED IT Time per tour = (set-up + walk ÷ 0.8 m/s + lines × 25 s) × 1.10 for delays (large orders: pallet truck, 40 s a line). Today one tour per order, picks spread over all aisles = 23.77 h, × 1.31 for the 08:00 peak = 31.1 h. Design: fast-pick 1.9 + reserve 1.0 + large orders 6.9 + small parts 1.9 = 11.7 h.
Notes: PRESENTER: Arnau (Picking) · about 1:30 Today picking is the biggest block of labour. In our model it takes about 31.1 picker-hours a day: 23.8 hours of work, because every tour picks one order across the whole building, plus 7.4 hours of extra staff for the eight o'clock peak. Our design needs 11.7 hours. Orders are split by size: 84% are small and go on a trolley, large ones go straight onto a pallet. The 1,409 best-sellers sit in the fast-pick area, where 71% of lines are picked. One tour picks for many orders, and the put-to-light wall sorts them and checks every item, which protects accuracy. And work is released in three waves, so the morning peak disappears. These times are modelled, so we propose a time study before go-live. IF ASKED HOW WE CALCULATED IT: One formula for every tour: set-up time, plus walking distance divided by walking speed, plus lines times seconds per line, plus 10% for delays. Example, a fast-pick tour: 30.7 lines and 123 metres — 90 seconds plus 123 ÷ 0.8 plus 30.7 × 25 seconds, times 1.1, is 18.5 minutes, so 99 lines an hour. 188 lines a day ÷ 99 = 1.9 hours. The same for the reserve (1.0 h), large orders (6.9 h) and small parts (1.9 h): 11.7 hours. Today uses the same formula, but one order per tour (2.4 lines for a small order) with picks spread over all aisles: 23.77 hours, times 1.31 for peak staffing.

## Slide 9: A fixed trailer departure plan gets 65% of orders out within 24 hours and every wave staged before its trailer leaves
TODAY · OUR SOLUTION · PROCESSES · VALUE FOR DHL · ROADMAP
Source: shipments April–June 2025 (Assa Abloy & DHL Supply Chain, 2025); departure plan (Deliverable 2 §4.5); step by step: appendix "How we calculated: service"
Rachel · Shipping owner
Service today (measured) vs our design, %
Chart: 
| Orders out within 24 h (design: modelled) | Lines staged on time (design: target)
Today | 37 | 49.9
Our design | 65 | 98
The day plan: three waves feed 14 trailer departures
Waves
Trailers
W1
W2
W3
06:00
08:00
10:00
12:00
14:00
16:00
15 → 4
trailers at the doors at once on a busy day: parked all day today, max 4 of 5 doors with time slots
102 → 70 h
order to trailer for the slowest 10% of orders (measured → modelled)
How it works
1
Fixed slots. 14 trailer slots a day, each with a time and a door; every wave ends at least 45 minutes before its trailers leave.
2
Same-day lane. Orders received before 12:00 (32%) go in wave 3 and leave the same day.
3
Pack and stage by departure. 4 pack stations; one staging lane per door, 46% full on the busiest afternoon.
HOW WE CALCULATED IT 65% = each of the 8,774 real orders re-timed: wave by arrival time (after 12:00 → wave 1 next morning), wave end + 45 min packing, then the first slot of its own carrier; share ≤ 24 h. ≥ 98% on time is the target the plan is built for, not a result. 15 = trailers standing at once on a busy day (p90, WMS arrive/dispatch times).
Notes: PRESENTER: Rachel (Shipping) · about 1:30 Shipping turns the whole day into one plan. Each carrier gets fixed departure slots and a door — 14 trailers a day — and the waves are planned backwards from those times, so every wave ends at least 45 minutes before its trailers leave. Orders that arrive before noon go in the third wave and leave the same day. The effect: 65% of orders leave within 24 hours instead of 37%, and the slowest ten percent drop from 102 to 70 hours. The yard calms down too: today up to 15 trailers stand parked; with time slots at most 4 of the 5 doors are busy at once. IF ASKED HOW WE CALCULATED IT: We took all 8,774 real orders from the data and gave each one a new departure time: its wave depends on when it arrived (after noon it goes in wave 1 the next working morning), then 45 minutes for packing after the wave ends, then the first departure slot of its own carrier. Then we compared the new departure with the arrival time: 65% leave within 24 hours, median 22 hours. The 98% on time is not a calculation — it is the target the plan is built for, because every wave ends 45 minutes before its trailers leave. Today's 49.9% is measured.

## Slide 10: For DHL: a kept service promise, €101k lower labour cost a year, and process changes that pay back in ~1.6 years
TODAY · OUR SOLUTION · PROCESSES · VALUE FOR DHL · ROADMAP
Source: cost model (Deliverable 3 §3): racking prices (IndexBox, n.d.; T-Racking, n.d.); labour €20 per hour (Rogier, course teacher, personal communication, October 2026); benchmark prices, not quotes; step by step: appendix "How we calculated: money"
Rachel · presenter
What changes for DHL
 | KPI | Today | Our design
Service | Lines staged on time | 49.9% | ≥ 98% (target)
 | Orders out within 24 hours | 37% | 65%
Cost | Picker-hours a day | ~31 | ~12
 | Cost per order line (incl. depreciation) | — | €3.09
Docks | Trailers at the doors at once | 15 | max 4
Safety | Pick faces with reach-truck traffic | — | none (100% separated)
Growth | +50% volume needs | — | +1 reach truck, +1 pallet truck, same 5 doors
Three ways to invest, € million
payback = investment ÷ labour saved a year
Chart: 
| Process changes only · 1.6 yrs | Full design, re-using racks · 5 yrs | Full design, new racks · 16 yrs
Investment | 0.16 | 0.52 | 1.63
€101k
labour saved a year
€342k
running cost a year (85% labour)
HOW WE CALCULATED IT Saving = 19.443 h a day ÷ 7.5 × 8 paid h × 244 days × €20 = €101,208. Payback = investment ÷ saving: €156,708 ÷ €101,208 = 1.55 years. Cost per line = (running cost €341,548 + depreciation €141,591) ÷ (640 lines × 244 days) = €3.09.
Notes: PRESENTER: Rachel (Shipping) · about 1:30 What does DHL get? On service, the promise to Assa Abloy is kept: a target of at least 98% of lines on time and 65% of orders out within 24 hours. On cost, about 12 picker-hours a day instead of 31, which saves about €101k a year, and a cost of €3.09 per order line that DHL can use in pricing. Reach trucks and pickers never share an aisle, and volume can grow by half with one extra reach truck and one extra pallet truck, through the same doors. On the right, three ways to invest. The process changes alone cost €0.16M and pay back in about 1.6 years. The full design costs €0.52M if today's racks can be re-used, or €1.63M with new racks, which pays back much more slowly. These are benchmark prices, not quotes. IF ASKED HOW WE CALCULATED IT: Saving: 12.073 hours a day from batching and the fast-pick area plus 7.370 hours from no peak staffing = 19.443 hours. Divided by 7.5 productive hours and times 8 paid hours, times 244 working days = 5,060.4 paid hours a year, times €20 = €101,208. Process investment: carton flow, shelves, trolleys, totes, put-to-light wall, WMS set-up and scanners = €142,462, plus 10% contingency = €156,708. Divided by €101,208 a year = 1.55 years. Cost per line: running cost €341,548 plus depreciation €141,591 = €483,139 a year, divided by 156,160 lines a year (640 × 244).

## Slide 11: Start with the low-cost process changes, then build the fast-pick area — the racking decision comes last
TODAY · OUR SOLUTION · PROCESSES · VALUE FOR DHL · ROADMAP
Source: proposed sequence based on the cost model (Deliverable 3 §3) and the hours saved per change; open points in the appendix
Gleb · presenter
Step 1 Change how work flows
Step 2 Build the fast-pick area
Step 3 Decide the racking
WHAT
Three waves a day, fixed trailer slots, slotting by demand, and dead stock cleared (21% of loads are over a year old).
DELIVERS
No 08:00 peak staffing: −7.4 picker-hours a day (~€38k a year), and the wave plan behind 65% within 24 h.
NEEDS
WMS wave set-up; carriers agree to fixed slots.
WHAT
Carton flow for the 1,409 best-sellers, the put-to-light wall, trolleys and scanners; small parts to bin shelving.
DELIVERS
Batch picking: −12.1 picker-hours a day (~€63k a year); 1,005 rack places freed.
NEEDS
Steps 1 + 2: €0.16M, payback ~1.6 years; small-parts shelving €69k.
WHAT
Re-use today's racking or install new single-deep racks; keep the 12th module in reserve for growth.
DELIVERS
8,960 places, every pallet reachable without moving another.
NEEDS
Re-use: €0.52M in total (payback ~5 years). New: €1.63M (~16 years).
Decisions we need from DHL: the 7,000 m² scope · carriers accepting fixed slots · re-use or replace the racking
Notes: PRESENTER: Gleb (Storage) · about 1:00 How to get there? We propose three steps. Step one changes how work flows: three waves, fixed trailer slots, slotting by demand and clearing dead stock. That needs little more than WMS settings and an agreement with the carriers, and it already removes the morning peak. Step two builds the fast-pick area and the put-to-light wall; together with step one that costs €0.16M and pays back in about 1.6 years. Step three is the racking decision, which is the big investment, so it comes last and depends on whether today's racks can be re-used. To start, we need three decisions from DHL: the 7,000 square metre scope, the carriers' acceptance of fixed slots, and the racking. Thank you — we are happy to take your questions; the appendix has every calculation step by step. IF ASKED HOW WE CALCULATED IT: Hours per step come from the picking model: the waves remove the 7.4 hours of peak staffing; batching and the fast-pick area take the work from 23.8 to 11.7 hours, 12.1 hours less. Hours become euros as on the value slide.

## Slide 12: Thank you — questions?
Vidhi — Receiving
Gleb — Storage
Arnau — Picking
Rachel Selvarathnam — Shipping
Notes: PRESENTER: All · about Q&A Each owner answers questions about their own process. The appendix starts with six 'How we calculated' slides (storage — Gleb, picking — Arnau, service and money and running cost — Rachel, receiving — Vidhi), then the four V's, the option choice, all KPIs, costs, open points, planning and control, equipment and sources.

## Slide 13: Storage: 8,512 occupied − 1,005 freed = 7,507 needed of 8,960 places (84%); at +16% a quarter the racks are full in ~4 months
HOW WE CALCULATED: STORAGE
Source: stock snapshots 1 April, 1 May, 1 June 2025 (Assa Abloy & DHL Supply Chain, 2025); layout drawing (Deliverable 2 §2); performance_cost.py
Gleb · answers
# | Step | How we calculated it | Result | Type
1 | Occupied places at the peak | highest of the three stock snapshots: 1 Apr 7,715 · 1 May 8,149 · 1 Jun 8,512 | 8,512 | data
2 | Places freed by small parts | rack places holding only small, slow items (whole stock ≤ 50 L; each ≤ 20 L, ≤ 15 kg, ≤ 60 cm; class C) — their 2,657 items move to bin shelving | 1,005 | data + rule
3 | Places needed in the design | 8,512 − 1,005 | 7,507 | model
4 | Places in the design | counted on the to-scale drawing: 7,776 standard + 864 odd-size + 320 long-goods | 8,960 | design
5 | Fill at the peak | 7,507 ÷ 8,960 (target ≤ 90%) | 84% | model
6 | Stock growth | (8,512 ÷ 7,715)^1.5 − 1 — growth over 2 months (April → June) turned into a quarter | +15.9% a quarter | model
7 | Months until full | ln(8,960 ÷ 7,507) ÷ ln(1.159) × 3 months — how many quarters of growth fit | 3.6 months | model
8 | With the reserved 12th module | ln((8,960 + 864) ÷ 7,507) ÷ ln(1.159) × 3 months | 5.5 months | model
9 | Dead stock | loads in the 1 June snapshot booked in more than 365 days earlier ÷ all 11,015 loads | 21% | data
Type: data = measured in Assa Abloy's WMS data · model = our calculation · assumption / benchmark = written down with its source · target = what the design is built to reach. Figures are rounded; the model works with unrounded values.
Notes: PRESENTER: Gleb (Storage) · about - Use when asked how the storage need, the fill rate or the 4 months were calculated.

## Slide 14: Picking: the same order lines timed per tour — one order per tour today (31.1 h with peak staffing), batched tours in the design (11.7 h)
HOW WE CALCULATED: PICKING
Source: WMS order lines April–June 2025 (Assa Abloy & DHL Supply Chain, 2025); time standards are assumptions A025 (to measure in a time study); picking_plan.py, performance_cost.py
Arnau · answers
Time per tour = (set-up + walking distance ÷ speed + lines × time per line) × 1.10 for delays set-up 90 s (trolley) / 180 s (pallet) · speed 0.8 m/s walking, 1.01 m/s pallet truck · 25 s per line (small orders) / 40 s (large orders)
# | Step | How we calculated it | Result | Type
1 | Today: one tour per order | 120 small orders (2.4 lines) and 23 large orders (14.9 lines) a day; picks spread over all 10 reserve aisles, because slotting does not follow demand | 23.77 h | model
2 | Today: staffed for the peak | 23.77 × 1.31 (picks in the 08:00 hour ÷ the average picking hour, measured) | 31.1 h | model
3 | Design: fast-pick trolley tours | 30.7 lines, 123 m: (90 + 123 ÷ 0.8 + 30.7 × 25) × 1.10 = 18.5 min → 99 lines/h; 188 lines ÷ 99 | 1.9 h | model
4 | Design: reserve trolley tours | 16 lines, 471 m → 19.8 min → 49 lines/h; 50 lines ÷ 49 | 1.0 h | model
5 | Design: large orders on a pallet | 23 orders × 18 min (13.1 lines, 279 m by pallet truck) | 6.9 h | model
6 | Design: small-parts shelving | 93 lines ÷ 50 lines/h (benchmark for shelving) | 1.9 h | model
7 | Design total | 1.9 + 1.0 + 6.9 + 1.9 | 11.7 h | model
8 | Hours saved a day | 31.1 − 11.7: 12.1 h from batching + fast-pick area, 7.4 h from no peak staffing | 19.4 h | model
Type: data = measured in Assa Abloy's WMS data · model = our calculation · assumption / benchmark = written down with its source · target = what the design is built to reach. Figures are rounded; the model works with unrounded values.
Notes: PRESENTER: Arnau (Picking) · about - Use when asked how the picker-hours were calculated. The time standards are assumptions, so the honest answer is: the method is sound, the seconds per line must be measured on the floor.

## Slide 15: Service: each of the 8,774 real orders is re-timed with the wave plan — 65% would leave within 24 hours (today 37%)
HOW WE CALCULATED: SERVICE
Source: WMS order and trailer times April–June 2025 (Assa Abloy & DHL Supply Chain, 2025); departure plan (Deliverable 2 §4.5); performance_cost.py, dock_mhe_plan.py
Rachel · answers
# | Step | How we calculated it | Result | Type
1 | Lead time today | per order: trailer dispatched − order received (WMS time stamps), 8,774 orders | median 25 h · p90 102 h · 37% ≤ 24 h | data
2 | Wave of each order | received before 06:00 → wave 1 (ends 09:30); before 09:30 → wave 2 (ends 12:45); before 12:00 → wave 3 (ends 15:15); after 12:00 or at the weekend → wave 1 of the next working day | — | design
3 | Ready to ship | wave end + 45 min for packing and staging | — | assumption
4 | Departure | first slot of the order's own carrier after it is ready (14 slots a day, 10:30–16:45) | — | design
5 | Lead time in the design | departure − order received, for the same 8,774 orders | median 22 h · p90 70 h · 65% ≤ 24 h | model
6 | On time today | share of order lines not flagged 'LATE' in the WMS (definition to confirm with DHL, A005) | 49.9% | data
7 | On time in the design | not calculated: every wave ends at least 45 min before its trailers leave, so the plan is built for this | ≥ 98% | target
8 | Trailers at the doors | today: on each day the most trailers standing at the same time (arrive → dispatch), p90 of the days; design: 25-min slots in the plan | 15 → max 4 | data / design
9 | Orders arriving 15:00–17:00 | orders with an arrival time in the 15:00 or 16:00 hour ÷ all orders | 55% | data
Type: data = measured in Assa Abloy's WMS data · model = our calculation · assumption / benchmark = written down with its source · target = what the design is built to reach. Figures are rounded; the model works with unrounded values.
Notes: PRESENTER: Rachel (Shipping) · about - Use when asked how the 65% and the lead times were calculated, or why 98% is a target.

## Slide 16: Money: 19.4 picker-hours saved a day = €101k a year; the €0.16M process changes pay that back in 1.55 years
HOW WE CALCULATED: MONEY
Source: cost register (Deliverable 3 §3, data/assumptions.json A030–A046); prices (IndexBox, n.d.; T-Racking, n.d.) and other benchmarks; labour (Rogier, course teacher, personal communication, October 2026); performance_cost.py
Rachel · answers
# | Step | How we calculated it | Result | Type
1 | Hours saved a day | 12.073 h (batching + fast-pick area) + 7.370 h (no peak staffing) | 19.443 h | model
2 | Paid hours a year | 19.443 h ÷ 7.5 productive h × 8 paid h × 244 working days | 5,060.4 h | assumption
3 | Labour saved a year | 5,060.4 h × €20 per hour | €101,208 | assumption
4 | Process investment | 31 carton-flow bays × €1,800 + 36 shelf bays × €200 + 6 trolleys × €433 + 54 totes × €16 + 120 put-to-light slots × €150 + installation €12,000 + WMS set-up €25,000 + 14 scanners × €1,500 = €142,462; + 10% contingency | €156,708 | benchmark
5 | Payback, process changes | €156,708 ÷ €101,208 a year | 1.55 years | model
6 | Full design, re-using racks | (all non-rack items €249,311 + 8,960 places × €25 to re-assemble) × 1.10 | €520,642 · 5.1 yrs | benchmark
7 | Full design, new racks | 8,640 places × €130 + 320 long × €160 + protection €58,240 + non-rack items €249,311, × 1.10 | €1,630,146 · 16.1 yrs | benchmark
8 | +50% volume | peak-day equipment hours × 1.5 ÷ (7.5 h × 80% use) → reach trucks 2 → 3, pallet trucks 3 → 4; doors = busiest-hour door need × 1.5 | 5 of 5 doors | model
Type: data = measured in Assa Abloy's WMS data · model = our calculation · assumption / benchmark = written down with its source · target = what the design is built to reach. Figures are rounded; the model works with unrounded values.
Notes: PRESENTER: Rachel (Shipping) · about - Use when asked how the saving, the investment or the payback were calculated. Prices are benchmarks with a low-high range in the cost register, not supplier quotes.

## Slide 17: Running cost: €342k a year plus €142k depreciation, over 156,160 order lines = €3.09 per line
HOW WE CALCULATED: RUNNING COST
Source: capacity plan (Deliverable 2 §6) and cost register (Deliverable 3 §3); lease and price benchmarks (IndexBox, n.d.; T-Racking, n.d.); labour (Rogier, course teacher, personal communication, October 2026); performance_cost.py
Rachel · answers
# | Step | How we calculated it | Result | Type
1 | Direct labour | 35.2 work-hours a day, receiving to loading (capacity plan) ÷ 7.5 × 8 × 244 days = 9,161.4 paid h × €20 | €183,228 | model
2 | Container crew | 2 people × 3 h × 1 container a day ÷ 7.5 × 8 × 244 days = 1,561.6 paid h × €20 | €31,232 | assumption
3 | Team leader + admin | 1.5 FTE × 8 h × 244 days = 2,928 h × €26 (mix of €27 and €24) | €76,128 | assumption
4 | Truck lease | (2 reach × €900 + 3 pallet × €150 + 2 rider × €350) × 12 months | €35,400 | benchmark
5 | Energy and upkeep | truck electricity €1,660 + rack inspection €2,500 + IT support €11,400 | €15,560 | assumption
6 | Running cost (OPEX) | sum of the rows above | €341,548 | model
7 | Depreciation | each investment ÷ its life: racks 15 years, equipment 7, IT 5 | €141,591 | model
8 | Cost per order line | (€341,548 + €141,591) ÷ (640 lines × 244 days = 156,160) | €3.09 | model
9 | Cost per order | €483,139 ÷ (144 orders × 244 days = 35,136) | €13.75 | model
Type: data = measured in Assa Abloy's WMS data · model = our calculation · assumption / benchmark = written down with its source · target = what the design is built to reach. Figures are rounded; the model works with unrounded values.
Notes: PRESENTER: Rachel (Shipping) · about - Use when asked how the running cost or the cost per order line were calculated. Labour is the biggest part; €20 per hour is the teacher's figure, €28 the high case.

## Slide 18: Receiving: loads per day from the stock snapshots; container and trailer times from a 20-minute dock call plus handling time
HOW WE CALCULATED: RECEIVING
Source: stock snapshots and inbound receipts (Assa Abloy & DHL Supply Chain, 2025); Jungheinrich truck data (Jungheinrich, 2019); capacity_plan.py, dock_mhe_plan.py, design_evaluation.py
Vidhi · answers
# | Step | How we calculated it | Result | Type
1 | Inbound loads a day | loads booked in during the 14 days before each snapshot ÷ receiving days: 70.9 · 108.2 · 117.6 → average (a lower bound: loads already shipped are not visible) | 98.9 (busiest day 167) | data
2 | Loose in containers | share of those loads with an Asian country of origin: 21.6% · 54.0% · 47.7% → average | 41% | data
3 | Container door time | 20 min docking and paperwork + 3 h unpacking by 2 people (A019) | 3.3 h | assumption
4 | Pallet trailer at the door | 20 min + 58.3 pallets × 0.99 min unloading with the ERE 225 | 1.3 h | model
5 | Dock-to-stock, pallet trailer | 20 min + 58.3 pallets × 1.19 min (putaway 2.38 min ÷ 2 reach trucks — slower than unloading) | 1.5 h (benchmark < 3.5 h) | model
6 | Container zone fit | m² per container = (24 conveyor lane + 3 per item + 1.9 per pallet, max 35 + 16 wrap/label) × 1.3 walkways, for the 568 containers in the data | 91% fit 190 m² · 97% fit 321 m² | model
7 | Inbound doors | average day: a pallet trailer (1.3 h) and a container (3.3 h) can arrive at the same time → 2 doors; ~8 smaller trucks a day would need 3 | 3 doors | model
8 | Outbound doors | busiest hour (p90): 9 trailers × their average time at the door ÷ (60 min × 85% door use) = 3.1 doors → 4 needed + 1 spare | 5 doors | model
Type: data = measured in Assa Abloy's WMS data · model = our calculation · assumption / benchmark = written down with its source · target = what the design is built to reach. Figures are rounded; the model works with unrounded values.
Notes: PRESENTER: Vidhi (Receiving) · about - Use when asked how the loads per day, the container time, dock-to-stock or the door numbers were calculated. The 3 hours unpacking is an assumption to confirm with DHL.

## Slide 19: Assa Abloy is a high-variety, medium-volume operation: many small, different orders with sharp peaks
OPERATION PROFILE
Source: WMS data April–June 2025 (Assa Abloy & DHL Supply Chain, 2025); four V's and process types (Slack et al., 2022); Deliverable 1 §11
VOLUME
MEDIUM
640
order lines a day (~144 orders)
99 inbound loads and ~15 outbound trailers a day
For the design: standard methods, scanning and batching pay off
VARIETY
HIGH
4,354
different items shipped in three months
5,291 items in stock; each, case and pallet picks; 138 hazardous items
For the design: several storage types; pick by order size
VARIATION
HIGH
1.8×
busiest day vs an average day (order lines)
08:00 pick peak 1.31× the average hour; stock +16% per quarter
For the design: level the self-made peak with waves; keep storage headroom
VISIBILITY
LOW
Low
customers see only the result
business customers and web shops (5% of lines) want complete, on-time orders
For the design: efficiency is designed in the back office, but the dispatch promise must be kept
So what: high variety at medium volume sits between a batch and a mass process — people supported by scanners, carton flow and a put-to-light wall fit better than full automation.
Notes: PRESENTER: Appendix · about - Use if asked what kind of operation this is (four V's, Slack et al.).

## Slide 20: We chose Option B, 'hybrid density': it scores highest (3.75 of 5) and stays ahead when cost counts most
OPTION CHOICE
Source: team decision matrix (Deliverable 1 §14–15); storage and picking systems (HAN University of Applied Sciences, 2026a); batch picking (de Koster et al., 2007)
Criterion | Weight | A Conventional+ | B Hybrid density | C Semi-automated
Space fit (7,000 m²) | 20% | 2 | 4 | 5
Labour efficiency | 20% | 2 | 4 | 5
CAPEX (lower is better) | 15% | 5 | 3 | 1
Travel / throughput | 15% | 2 | 4 | 5
Flexibility | 10% | 5 | 4 | 2
Simplicity / low risk | 10% | 5 | 3 | 2
Peak resilience | 10% | 2 | 4 | 4
Weighted score (max 5) | 100% | 3.05 | 3.75 | 3.70
Scores 1 (poor) to 5 (best), agreed in the team. Weighted score = sum of weight × score; for B: 0.20×4 + 0.20×4 + 0.15×3 + 0.15×4 + 0.10×4 + 0.10×3 + 0.10×4 = 3.75.
Why B
1
Fits the site with all working areas: 6,731 m² of 7,000 m².
2
Cuts labour through slotting and batch picking, without betting on automation.
3
Proven kit at moderate cost: reach trucks, carton flow, a put-to-light wall.
Robustness: scores with other weights
Weights | A | B | C
Base case | 3.05 | 3.75 | 3.70
Cost-driven | 3.35 | 3.65 | 3.35
Space-driven | 3.55 | 4.75 | 4.85
Only when space is all that counts does C edge ahead (4.85 vs 4.75).
Notes: PRESENTER: Appendix · about - Use if asked why not more automation, or how the option was chosen.

## Slide 21: Nine KPIs, each with an owner, track the five performance objectives — all but storage headroom meet their target
KPI SCORECARD
Source: KPI overview (Deliverable 3 §2); today = WMS data April–June 2025 (Assa Abloy & DHL Supply Chain, 2025); benchmarks (Extensiv, n.d.); design values modelled
Objective | KPI | Today | Our design | Target | Owner | Status
Dependability | On-time shipment (lines staged before departure) | 49.9% | ≥ 98% (target) | ≥ 98% | Rachel | ● meets
 | Trailers at the doors at once (busy day) | 15, parked | max 4 | ≤ 5 | Rachel | ● meets
Speed | Orders out within 24 hours | 37% | 65% | ≥ 60% | Rachel | ● meets
 | Dock-to-stock, pallet trailer | 1–3 days (big receipts) | ~1.5 h | < 3.5 h | Vidhi | ● meets
Quality | Pick accuracy (orders without error) | not in the data | ≥ 99.7% (target) | ≥ 99.3% | Arnau | ● meets
Cost | Fast-pick hit rate (lines from the fast-pick area) | — | 71% | ≥ 60% | Arnau | ● meets
 | Rack fill at the peak | 8,512 places used | 84% | ≤ 90% | Gleb | ● meets
Flexibility | Containers unpacked inside their zone | — | 91% | ≥ 90% | Vidhi | ● meets
 | Storage headroom | — | ~4 months | ≥ 12 months | Gleb | ● gap
Checked every day in the start-of-day meeting of the four owners and weekly with the DHL operations manager (Deliverable 2 §7.5).
Notes: PRESENTER: Appendix · about - Use if asked how the design is measured, or who owns which KPI.

## Slide 22: The full fit-out costs €1.63M, mostly new racking; running the warehouse costs €342k a year
COST DETAIL
Source: cost model (Deliverable 3 §3): racking prices (IndexBox, n.d.; T-Racking, n.d.); labour €20 per hour (Rogier, course teacher, personal communication, October 2026); benchmark prices, not supplier quotes
Investment (CAPEX) by group, € thousand
Chart: 
| Storage racks | Contingency | Small-item storage | Picking | Sorting & packing | IT | One-off (moving, training) | Container zone
CAPEX | 1233 | 148 | 69 | 66 | 50 | 46 | 11 | 6
Contingency = 10% of all items.
€291k
labour a year (direct and indirect staff)
€37k
machinery a year (truck lease and energy)
€3.09
per order line (€13.75 per order), depreciation included
€20.02
per inbound pallet received and put away
Notes: PRESENTER: Appendix · about - Use if asked for the cost breakdown.

## Slide 23: Four open points to close before go-live — each has an owner and a next step
OPEN POINTS
Source: assumption register (Deliverable 2 §8) and risks in Deliverable 3
OPEN POINT
IMPACT
NEXT STEP
OWNER
1
Stock growth
racks full in ~4 months at +16% per quarter
Clear dead stock (21% of loads over a year old); order the reserved 12th module at 90% fill (+864 places)
Gleb
Storage
2
Pick times are modelled
they set the staff per wave; labour is 85% of the running cost
Time study on the current floor; recalculate pickers per wave
Arnau
Picking
3
Costs are benchmarks
racking alone ranges €80–200 per place
Quotes for racking, carton flow and the put-to-light wall; lease quote from Jungheinrich
Rachel
Shipping
4
Hazard class unconfirmed
138 items, 2,197 loads, 385 t in stock
Ask Assa Abloy for UN numbers and safety data sheets; size the hazmat section
Vidhi
Receiving
Notes: PRESENTER: Appendix · about - Use if asked about risks or what happens before go-live.

## Slide 24: Planning and control: one day plan links the four processes, and each owner checks their KPIs every day
PLANNING AND CONTROL
Source: Deliverable 2 §7 (planning and control per process)
Process (owner) | Planned ahead | Controlled during the day | KPIs
Receiving Vidhi | a time slot for every delivery from the advance shipping notice; containers booked on R1 in the morning | late or early arrivals re-booked into the next free slot | dock-to-stock, container door time
Storage Gleb | system-directed putaway; min/max refills between the waves; re-slotting every month | cycle counts (A monthly, B quarterly, C yearly); occupancy each month, 12th module ordered at 90% | rack fill, storage headroom
Picking Arnau | three waves planned back from the departures; pickers per wave = lines ÷ pick rate | lines picked against plan per hour; the wall releases only complete, correct orders | pick rate, accuracy, picker-hours
Shipping Rachel | 14 fixed trailer slots; pack and stage in departure order | checked after each departure; a missed slot moves to the carrier's next slot | on-time shipment, orders within 24 h
THE CONTROL LOOP
Measure: scans in the WMS
Compare with the target
Act: re-plan or re-slot
Check: KPI back on target
Every day: start-of-day meeting of the four owners · every week: KPI review with DHL · every month: review with Assa Abloy
Notes: PRESENTER: Appendix · about - Use if asked how the design is planned and controlled day to day.

## Slide 25: Equipment: the fleet covers the peak day; at double volume the 5 outbound doors, not the trucks, become the limit
EQUIPMENT
Source: Deliverable 2 §5 and Deliverable 3 stress test; equipment data (Jungheinrich, n.d.-a, n.d.-b, 2019)
Equipment plan
Equipment | Task | Units | Busy, avg day
ETV 216i | Putaway + replenishment + full-pallet picks | 2 | 33%
EJE 120i | Large orders: pick-to-pallet (one order per pallet) | 3 | 31%
ERE 225 | Unload trailers/containers, load outbound, dock moves | 2 | 14%
Pick trolley (3-tier, 6 totes) + totes | Small orders: zone batch picking, sorted at the put-wall | 6 | —
Units = recommended fleet, sized for the peak day: peak equipment-hours ÷ (7.5 h × 80% use). Busy = equipment-hours ÷ available hours on an average day.
Stress test: what more volume needs
Volume | Staff (peak FTE) | Reach trucks | Pallet trucks | Out doors
100% | 8.7 | 2 | 3 | 4
150% | 13.1 | 3 | 4 | 5
200% | 17.5 | 4 | 5 | 7
250% | 21.8 | 4 | 6 | 8
Every number in the table = today's peak-day need × the volume factor, rounded up. The design has 5 outbound doors; above that, more time slots spread the trailers over the day.
Notes: PRESENTER: Appendix · about - Use if asked about equipment, utilisation or growth.

## Slide 26: Sources
SOURCES
References in APA 7th edition. Personal communications are cited in the text only.
Assa Abloy, & DHL Supply Chain. (2025). Assa Abloy storage details (1 April, 1 May and 1 June 2025) and outbound details (April–June 2025) [Unpublished raw data]. DHL Supply Chain, Bemmel.
de Koster, R., Le-Duc, T., & Roodbergen, K. J. (2007). Design and control of warehouse order picking: A literature review. European Journal of Operational Research, 182(2), 481–501. https://doi.org/10.1016/j.ejor.2006.07.009
Extensiv. (n.d.). 3PL fulfillment KPIs: Formulas & benchmarks. Retrieved October 18, 2026, from https://www.extensiv.com/blog/3pl-fulfillment-kpis-formulas-benchmarks
HAN University of Applied Sciences. (2026a). [Lecture slides on warehouse design, layouts, storage and order-picking systems, week 3]. OPERMB04 Operations Management. Unpublished course material.
HAN University of Applied Sciences. (2026b). Project DHL on the move: Project OTM [Unpublished project brief]. OPERMB04 Operations Management.
IndexBox. (n.d.). European Union: Metal racks market analysis, forecast, size, trends and insights. Retrieved October 18, 2026, from https://www.indexbox.io/store/european-union-metal-racks-market-analysis-forecast-size-trends-and-insights/
Jungheinrich. (n.d.-a). EJE 120i: Technical data (JEHN0398) [Data sheet]. Logisnext Americas. Retrieved October 14, 2026, from https://www.logisnextamericas.com/globalassets/migration-blocks/jungheinrich/product-listing/pallet-trucks/eje-120-225/jehn0398---eje-120i-spec-sheet.pdf
Jungheinrich. (n.d.-b). ERE 225 rider pallet truck [Product listing]. Retrieved October 7, 2026, from https://www.shop.jungheinrich.co.uk/en/ere-225---98280668
Jungheinrich. (2019). ETV 216i: Technical data [Data sheet]. Retrieved October 7, 2026, from https://www.fallsway.com/hubfs/Fallsway_January2022/Pdf/jungheinrich-ii-etv-216i-spec-sheet-english.pdf
Slack, N., Brandon-Jones, A., & Burgess, N. (2022). Operations management (10th ed.). Pearson.
T-Racking. (n.d.). How much does pallet racking cost? Retrieved October 18, 2026, from https://t-racking.com/how-much-does-pallet-racking-cost
Notes: PRESENTER: Appendix · about - All sources used on the slides; the full list is in the portfolio.